4

Shipper‘s Declaration for Dangerous Goods

- Instructions -

The Shipper’s Dangerous Goods (DG) template and a completed sample Dangerous Goods (DG) Form for GalliaPharm® can be found at: www.radiopharma.com/disposal and is also included with your Return Kit.

Please note that the DG form must be typed and signed by a qualified & trained shipper.

- Complete Shipper and Consignee boxes in upper left side.

You are the Shipper, and Eckert & Ziegler Isotope Products, 1800 N Keystone Street, Burbank, CA 91504 is the Consignee.

- Transportation Details:

- Airport of Departure: Contact your local FedEx office for location

code.

- Airport of Destination: LAX

- For returns for waste disposal only (e.g. decayed generators): cross out “Passenger and Cargo Aircraft”

- Air Waybill #: this is a 12 digit tracking # from your FedEx 
Air Waybill

- Shipper’s Reference No.: notate EZ issued Return Number (RA#)

- Shipment Type: cross out “Non-Radioactive”

- Nature & Quantity of Dangerous Goods:

- UN or ID #: UN2915

- Proper Shipping Name: Radioactive material, Type A  package

- Class or Division: 7

- Packaging Group: skip this field

- Quantity and type of packaging: enter “Ge-68, solid oxide”, Activity in MBq, and number of Type A Packages

- Packaging Instructions: II Yellow, TI, & dimensions of box in 
centimeters

- Authorization: skip this field

- Shipper’s 24 hour Emergency Telephone Phone Number

Under “Additional Handling Information”, record the Shipper’s 24 hour Emergency phone #. This is your 24 hour telephone number should an emergency arise with your package during transit. This number is also recorded on the Emergency Response / Return Packing List Sheet 2.

Once all information is typed, the DG form is complete

Print 3 copies on candy striped paper. If using a black & white printer, put the provided candy striped paper in your printer. The typed DG Form must have the colored candy stripe or it will be rejected by the carrier (i.e. FedEx).

Note: Shipper’s Declaration for DG Form must be completed and

signed by a qualified DOT trained shipper.

Regulatory References: Title 49 CFR 172.101, 172.204, 172.403,

172.704, 173.403, 173.425, 173.433. Other requirements may also 
apply.

Eckert & Ziegler Radiopharma GmbH	GalliaPharm® Return US – Form 4	SOP-00038-A.008 V3.0